## Slide 1: CyberShake Study 21.12: Say, what is that, anyway?
February 2022 SCEC Staff Meeting
Scott Callaghan

## Slide 2: From January 2022 staff slides…

## Slide 3: CyberShake Study 21.12
What is CyberShake?
What’s unique about Study 21.12?
What is CyberShake?

## Slide 4: Probabilistic Seismic Hazard Analysis (PSHA)
Quantifying hazard based on probabilities.
Pick a location.
Get a list of all possible earthquakes that might affect the site, along with their probabilities.
Calculate the amount of shaking each earthquake would cause at the site.
Combine the shaking values with the probabilities to produce a hazard curve.
2% in 50 yrs
0.45g

## Slide 5: Where do we get this list?
Called an ‘earthquake rupture forecast’, or ERF
Working Group on California Earthquake Probabilities produces ERFs
  UCERF2 (2008), UCERF3 (2015), ask Kevin about UCERF4 
  Derived from slip rates, event rates, deformation, other observables
Alternatively, can run a physics-based earthquake simulator, like RSQSim
  Simulates hundreds of thousands of years of California fault system
  Use the generated earthquakes as an ERF
Usually 50-600k earthquakes per site

## Slide 6: Probabilistic Seismic Hazard Analysis (PSHA)
Quantifying hazard based on probabilities.
Pick a location.
Get a list of all possible earthquakes that might affect this location, along with their probabilities.
Calculate the amount of shaking each earthquake would cause at your site.
Combine the shaking values with the probabilities to produce a hazard curve.

## Slide 7: Calculating Intensities
One way is to use ground motion prediction equations (GMPEs).
  Regressions on historic earthquake data
  Very quick to calculate
  Only able to capture simpler effects
CyberShake uses a “physics-based” approach
  Performs wave propagation simulations
  Captures complex physics
  Requires supercomputers
Distance
Ground Motion
M6.5

## Slide 8: Is CyberShake worth it?
Overall goal is to reduce hazard uncertainty
GMPEs deliver a mean + standard deviation. Larger deviations translate into higher hazard curves, requiring stronger buildings.
With CyberShake, we hope to be able to model additional physics to reduce uncertainty.
  For example, perhaps differences in ground structure which are rolled into ‘uncertainty’ in GMPEs can be modeled in CyberShake.
σ
σ
Single-event intensity distribution
∑
Hazard Curve

## Slide 9: Workflow Tools
CyberShake manages many jobs and files
  16,000 software executions
  103 million files
We use workflow tools (Pegasus, HTCondor) to help with all this
  Describes the software steps, their inputs, and their outputs
  Transfers files between workflow server, USC storage, and supercomputer
  Execute jobs automatically
  Restarts jobs if they fail
One workflow per site

## Slide 10: CyberShake Study 21.12
What is CyberShake?
What’s unique about Study 21.12?

## Slide 11: What’s special about this study, scientifically?
RSQSim earthquake simulator as source of ERF
Kevin and Bruce Shaw generated 715,000 years of California earthquakes
Builds on Kevin’s paper (presented at 10/20 staff meeting)
Entire Southern California hazard map (335 sites)
First fully physics-based PSHA model

## Slide 12: What’s special about this study, technically?
In summer 2021, moved our workflow server to USC CARC
  Many issues to resolve (storage, firewall, permissions, etc.)
  First CyberShake study with new server
First study to use the Summit supercomputer at Oak Ridge
  #2 on Top500 list
  70,000 node-hrs
Peak of 46% of Summit

## Slide 13: Results, 2 sec
Study 21.12
Ratio of Study 21.12 to UCERF2 CyberShake

## Slide 14: Results, 3 sec
Study 21.12
Ratio of Study 21.12 to UCERF2 CyberShake

## Slide 15: Now you know!