## Slide 1: Seismic Hazard Analysis Using Distributed Workflows
Scott Callaghan
Southern California Earthquake Center
University of Southern California
SC15

## Slide 2: Outline
Seismic Hazard Analysis
SCEC CyberShake
  Overview
  Technical Requirements
Scientific Workflows
  Advantages of workflow tools
CyberShake Study 15.4
  Challenges
  Results & Performance
Future Directions

## Slide 3: Seismic Hazard Analysis
What will peak ground motion be over the next 50 years?
  Used in building codes, insurance, government, planning
  Answered via Probabilistic Seismic Hazard Analysis (PSHA)
  Communicated with hazard curves and maps
Hazard curve for downtown LA
2% in 50 years
0.25 g
Probability of exceeding 0.1g in 50 yrs

## Slide 4: PSHA Process
Pick a location of interest.
Determine what future earthquakes might happen which could affect that location.
Estimate the magnitude and probability for each earthquake.

## Slide 5: PSHA Process, cont.
4. Determine the shaking caused by each earthquake at the site of interest (we use physics-based simulation)
5. Combine the levels of shaking with the probabilities from (3) to produce a hazard curve.

## Slide 6: SCEC CyberShake Project
Physics-based seismic hazard analysis
Began project in 2008
Continuous improvement in realism
Date | Study | Number of sites | Systems
6/08-7/08 | 0.5 | 9 | USC HPC, NCSA Mercury
4/09-6/09 | 1.0 | 223 | USC HPC, TACC Ranger
11/11-3/12 | 1.4 | 46 | USC HPC, TACC Ranger
10/12-3/13 | 2.2 | 268 | USC HPC, NICS Kraken
4/13-6/13 | 13.4 | 1144 | USC HPC, NCSA Blue Waters, TACC Stampede
2/14-3/14 | 14.2 | 1144 | USC HPC, NCSA Blue Waters

## Slide 7: Demand for Higher Frequencies
CyberShake runs to date with f = 0.5 Hz
Buildings most affected by
  Frequency = 10 / (height in floors)
Demand by building engineers for higher frequencies
CyberShake advanced to 1 Hz, ~16x computation

## Slide 8: Computational Requirements
Component | Data | Executions | Cores/exec | Node-hrs
Mesh generation | 120 GB | 1 | 3840 CPUs | 45
Tensor simulation | 1.5 TB | 2 | 800 GPUs | 1485
Seismogram synthesis (master/worker) | 30 GB | 1 | 3712 CPUs | 1220
Curve generation | 1 MB | 1 | 1 | < 1
Total | 1.6 TB | 5 |  | 2750
Tensor Creation
Post Processing
This is for one location of interest;
want to run many for a hazard map

## Slide 9: System Requirements
Need to be able to utilize large HPC systems
  2750 node-hrs/site x 300 sites ~ 1M node-hrs
  Must have GPUs for tensor calculation
Coordinate jobs across multiple systems
  USC HPC
  NCSA Blue Waters
  OLCF Titan
Data management
Automated for around-the-clock execution
We use scientific workflows

## Slide 10: Workflow Tools
We use Pegasus-WMS, HTCondor, Globus stack
Pegasus-WMS (USC/ISI)
  Use API to describe workflow as tasks with dependencies
  Plan workflow for execution on specific resource
  Adds data transfer jobs when needed
  Gideon Juve’s talk for more details
HTCondor (U of Wisconsin)
  Manages runtime execution of jobs
Globus (U of Chicago/ANL)
  GRAM: Protocol for remote job submission
  GridFTP: Fast transfer between sites

## Slide 11: Why these workflow tools?
Abstract vs. Concrete workflow
  Abstract workflow: algorithmic description of tasks with dependencies
  Concrete workflow: jobs and files are bound to paths on a specific system
  Since abstract workflow is the same between systems, only need to change the mappings for new systems
Data management
  Transfer intermediate data between systems
  Transfer output data to USC HPC filesystems
  Data products registered for discovery

## Slide 12: Why these workflow tools? (cont.)
Remote job submission
  Need to submit jobs to HPC systems automatically
  Interface with HTCondor and GRAM provides that
  Pilot jobs for systems which don’t support GRAM
Pegasus-MPI-cluster (PMC)
  Tool provided with Pegasus
  MPI wrapper around tasks
  Master-worker paradigm
  Converts many small jobs into 1 large efficient one
  Can run entire workflow this way

## Slide 13: CyberShake Study 15.4
CyberShake Study at 1 Hz
Included new locations, for 336 in total
New, more complex descriptions of earthquakes
Run on
  USC HPC
  NCSA Blue Waters
  OLCF Titan

## Slide 14: Workflows on Blue Waters
Want to run both GPU and CPU jobs
  22,500 CPU, 4,700 GPU nodes
Support for GRAM job submission
HTCondor on submit host at USC submits jobs to Blue Waters via GRAM
If job fails, retry
Advantages:
  All the logic is in the submit host
  Little overhead

## Slide 15: Workflows on Titan
Want to run GPU jobs
  18,700 GPU nodes
No support for GRAM
Use “pilot jobs”:
  Daemon on Titan monitors HTCondor queue at USC
  When tasks appear, daemon submits pilot job to Titan
  When pilot job starts, calls back to HTCondor collector
  Work is assigned to pilot job
Must be able to connect to collector from pilot job
Titan scheduler only knows about pilot job, not workflow jobs

## Slide 16: Workflows on Titan (cont.)
Used multiple pilot jobs with different sizes, lengths
  Can define job type to match with 1 kind of job
  Dependencies enforced with qsub
  Can vary the number of ‘slots’ (tasks per pilot job)
Balance in runtime between efficiency and failure
  Pilot jobs will terminate after idle time
  Will terminate at end of runtime, regardless of task
Pilot jobs have complexity and overhead
Can wrap jobs across multiple workflows
  Submitted jobs of up to 8000 (43%) nodes

## Slide 17: Execution Schematic
USC
Blue Waters
Titan
GRAM
GRAM to PBS
HTCondor
HTCondor queue
Blue Waters queue
Titan queue
Pilot daemon
Workflow task
Pilot job
Workflow task
Data products task
Pegaus workflow description
Transfer
job

## Slide 18: Study 15.4 Performance Metrics
Makespan: 914.2 hrs (38.1 days)
1.4 million node-hours
4372 jobs submitted
  3933 to Blue Waters via GRAM
  439 pilot jobs on Titan
Average of 1,962 nodes, with a max of 17,986 used
  20% of Blue Waters, 80% of Titan
On average, 53 workflows running concurrently
Managed 550 TB of data
  197 TB transferred from Titan to Blue Waters
  9.8 TB staged back to USC HPC disk (~7M files)
36.5% more efficient than 0.5 Hz runs

## Slide 19: Results
Hazard curves for 336 sites
For each site:
  500,000 seismograms
  Maximum shaking measures for each seismogram
  List of which ruptures contribute the most
Useful dataset for wide-ranging applications

## Slide 20: Future Directions: Broadband CyberShake
Building engineers looking for higher frequencies
  Prohibitive to simulate to 10 Hz
  Use stochastic technique to calculate 1-10 Hz seismograms
  Combine with Study 15.4 results
Requires 21,000 additional tasks per site
  Runtimes of <1 sec to 30 min
  Using Pegasus-mpi-cluster to manage execution

## Slide 21: Future Directions
Larger geographic region
  Good models exist for the Bay Area
  Working to improve models for Central California
New rupture forecast
  25x as many earthquakes to consider
  Some are very large; may need to approximate
Earthquake forecasting
  Use CyberShake ground motions and long-term simulators to make forecasts
  Test forecasts in SCEC CSEP testing center

## Slide 22: Questions?