## Slide 1: CyberShake Seismic Hazard Models for Central California
Scott Callaghan
SC17

## Slide 2: Probabilistic Seismic Hazard Analysis (PSHA)
What will peak earthquake shaking be over the next 50 years?
Useful information for:
  Building engineers
  Disaster planners
  Insurance agencies
PSHA performed by
  Assembling a list of earthquakes
  Determining how much shaking each event causes
  Combining the shaking levels with probabilities
2% in 50 yrs
0.4 g

## Slide 3: PSHA Approaches
Ground Motion Prediction Equations (GMPEs)
  Equations derived from historical data
Limited near-fault data
Limited large magnitude data
Large variability
Long tails
Simulation-based approach
  Reduce uncertainty by capturing complex physics
  Computationally expensive
6-7g

## Slide 4: SCEC CyberShake Project
3D physics-based platform for PSHA
For each site of interest:
  Determine nearby (<200 km) earthquakes
  Add variability to earthquakes
  Simulate each of 500,000 earthquakes
  Determine maximum shaking from each
  Combine with probabilities
Project began in 2007
Continual improvement

## Slide 5: CyberShake Data Flow
500,000 Seismograms
75M intensity measures
UCVM
AWP-ODC
Seismogram Synthesis
Mesh generation
1 job per site
MPI, 1500-4000 cores
SGT computation
2 jobs per site
MPI, 200-800 GPUs
Post-processing
500,000 jobs per site
MPI master/worker, 3712 cores
Data
Product Generation
Populate DB, construct images
6 jobs per site
CVM-S4.26
z = 6 km
Community Velocity Model
3 TB
data transfer
Uniform California Earthquake Rupture Forecast
Rupture Generator
hazard curves
CyberShake Hazard Map
Most recent CyberShake study took 4 weeks of real time and used 21 million core-hours

## Slide 6: CyberShake Requirements
200-400 sites needed for a hazard map
Execute jobs across multiple systems
  USC HPC, NCSA Blue Waters, OLCF Titan
Automated execution of jobs
Data management
  28,000 files and 30 GB output per site
  Migration of input and output files when needed
Error recovery
Decided to use scientific workflows

## Slide 7: CyberShake Workflow Tools
Pegasus-WMS (USC ISI)
  Use API to describe workflow as tasks with dependency
  Plan workflow for execution on specific resource(s)
  Adds data transfer jobs and metrics wrappers
  Intro to Pegasus Wed at 2; office hours Tues at 3 and Wed at 3
HTCondor (U of Wisconsin)
  Manages runtime execution of jobs
  Resolves dependencies
  Checkpoints workflows
Globus (booth #373)
  GRAM for communication between workflow host and remote system
  GridFTP for file transfer

## Slide 8: CyberShake in Central California
2017 science goal
Proof-of-concept that CyberShake can be moved outside of Southern California
New sites
New velocity model of earth’s crust
New workflow approach

## Slide 9: Central California Challenges
Simulation volume
  Had to combine multiple velocity models
  Smooth across interfaces
Targeted OLCF Titan for 200-node GPU jobs
  Requires two-factor authentication
  Difficult to automate job submission
  Tried pilot job approach in 2015; successful but with 32% overhead
  Looking for more efficient solution

## Slide 10: rvGAHP Workflow Approach
“reverse GAHP” – approach using HTCondor protocol
  Enables remote job submission without authentication to remote system
Daemon runs on remote system
Initiates connection to workflow submission host
Workflow can then use connection to submit jobs to remote queue
Opens up Titan to low-overhead workflows

## Slide 11: CyberShake Study 17.3
Conducted over 31 days in March-April 2017 on NCSA Blue Waters, OLCF Titan, USC HPC
2 models at 438 sites
Averaged 1295 nodes, max of 5374
  900,000 node-hrs (21.6M core-hrs)
Workflow tools scheduled 15,581 jobs
777 TB of data managed
  308 TB transferred
  10.7 TB archived on USC disks
Generated 285 million seismograms

## Slide 12: CyberShake Study 17.3 Results
Study 17.3
Combined map

## Slide 13: Future Directions
UCERF2
14,000 ruptures
UCERF3
350,000 ruptures
Move to new forecast
  UCERF 3
  RSQSim earthquake simulator
Run CyberShake in new regions – San Diego? Bay Area?
Add new physics
  Increase maximum frequency – applicable to more buildings
  Velocity model heterogeneities, fault roughness, topography
Optimize
  Seismogram synthesis – compress data? Large shared-memory nodes?
  Use machine learning to eliminate some earthquakes

## Slide 14: Thanks!