## Slide 1: SCEC Application Performance and Software Development
Yifeng Cui1, Thomas Jordan2, Philip Maechling2, Scott Callaghan2, Kim Olsen3, Jacobo Bielak4, Steven Day3, Ricardo Taborda5, Po Chen6, Patrick Small2, Daniel Roten1, Efecan Poyraz1 and SCEC CME Collaboration
1University of California at San Diego, 2Southern California Earthquake Center, 3San Diego State University, 4Carnegie Mellon University
5University of Memphis, 6University of Wyoming
OLCF Users Meeting, July 22-24, 2014

## Slide 2: SCEC Computational Pathways
Improvement of models
4
Invert
Other Data Geology
Geodesy
4
Ground-motion inverse problem (AWP-ODC, SPECFEM3D)
Physics-based
simulations
AWP = Anelastic Wave Propagation
NSR = Nonlinear Site Response
KFR = Kinematic Fault Rupture
DFR = Dynamic Fault Rupture
2
AWP
Ground
Motions
NSR
2
KFR
Ground motion simulation (AWP-ODC, Hercules)
Empirical
models
Standard seismic hazard analysis (RWG, AWP-ODC)
1
Intensity
Measures
Attenuation
Relationship
1
Earthquake Rupture
Forecast
“Extended” Earthquake Rupture Forecast
Structural Representation
3
AWP
DFR
3
Dynamic rupture modeling (SORD, AWP-ODC)
Hybrid MPI/CUDA
AWP-ODC – Yifeng Cui and Kim Olsen
Hercules – Jacobo Bielak and Ricardo Tarbora
SORD – Steven Day
CyberShake - Scott Callaghan
OpenSHA/UCERF3 - Kevin Milner
UCVM, CVM-H - David Gill
Broadband - Fabio Silva
AWP-ODC
AWP-ODC, Hercules

## Slide 3: AWP-ODC
Started as personal research code (Olsen 1994)
3D velocity-stress wave equations
solved by explicit staggered-grid 4th-order FD
Memory variable formulation of inelastic relaxation
using coarse-grained representation (Day 1998)
Dynamic rupture by the staggered-grid split-node (SGSN) method (Dalguer and Day 2007)
Absorbing boundary conditions by perfectly matched layers (PML) (Marcinkovich and Olsen 2003) and Cerjan et al. (1985)
Inelastic relaxation variables for memory-variable ODEs in AWP-ODC

## Slide 4: AWP-ODC Weak Scaling
94% efficiency
100% efficiency
2.3 Pflop/s
93% efficiency
(Cui et al., 2013)

## Slide 5
Hercules – General Architecture
» Finite-Element Method
» Integrated Meshing
(unstructured hexahedral)
» Uses and octree-based library for meshing and to order
elements and nodes in memory
End-to-End Simulation Process
Main Solving Loop
Most Demanding Operations
Octree-Based FE Mesh
» Explicit FE solver » Plane wave approximation to
absorbing boundary conditions
» Natural free surface condition
» Frequency Independent Q
Hercules was developed by the Quake Group at Carnegie Mellon University with support from SCEC/CME projects. Its current developers team include collaborators at the National University of Mexico, the University of Memphis, and the SCEC/IT team among others.
Jacobo Bielak (CMU) and Ricardo Taborda (UM) See Refs. Taborda et al. (2010) and Tu et al. (2006)

## Slide 6
I/O
Hercules on Titan – GPU Module Implementation
Modifications to Solver Loop
Source Forces
Stiffness,
Attenuation
Nonlinear
and Buildings
Comm
Forces
Comm
Disp
Disp Update
Reset
Original Solver Loop
CPU
I/O
Source Forces
Stiffness,
Attenuation
Nonlinear and Buildings
Comm
Forces
Comm
Disp
Disp Update
CPU
GPU Solver Loop
Reset
GPU
Sync point
Disp
Forces
Forces
Disp
(Patrick Small of USC and Ricardo Taborda of UM, 2014)
Chart: Stiffness and Attenuation Time
| CPU | GPU
 | 346.22 | 51.32
Chart: Displacement Update Time
| CPU | GPU
 | 29.92 | 12.36
Chart: Solver Time
| CPU | GPU
 | 561.1 | 236.94
Chino Hills 2.8 Hz, BKT damping, 1.5 B elements, 2000 time steps (512 compute nodes)

## Slide 7
Hercules on Titan – GPU Performance
Initial Strong Scaling Tests on Titan (in green) compared to other systems
Recent Hercules developments include GPU capabilities using CUDA
Performance tests for a benchmark 2.8 Hz Chino Hills simulation show near perfect strong and weak scalability on multiple HPC systems including TITAN using GPU
The acceleration ratio of the GPU code with respect to the CPU is of a factor of 2.5x overall. Larger factors are obtained in the specific modules where GPU was implemented
(Jacobo Bielak of CMU, Patrick Small of USC and Ricardo Taborda of UM, 2014)

## Slide 8
6
Simulations
1024
CPU cores
64
Nvidia GPUs
64
Compute Nodes
5713
Titan Core-Hours
ORNL
Hercules on Titan – Validation of La Habra
Resource Utilization

## Slide 9
MIRA
Hercules on Titan – Validation of La Habra
Modeling, Simulation and Validation Process
Combination of 3 SCEC Software Platforms (BBP, UCVM, High-F) across multiple HPC systems including TITAN at OLCF and other DOE (Mira) and NSF (Blue Waters) systems
Blue Waters
MIRA
USC HPC
TITAN
Source Inversion
Centroid Moment Tensor
BBP Extended
Source Generation
Standard Rupture Format
Extended and Point Source Models
Hercules (GPU Module)
CVM-S4
3D Tomographic Inversion
CVM-S4.26 Perturbations 3D Grid
UCVM Platform
CVM-S4 CVM-S4.26 Etrees
SCEC Data Center
Recorded Seismograms
Synthetic Seismograms
Desktop Computer
Post-processing
Validation (GOF Scores)
Plotting (Matlab + GMT)
SCEC Data Center
Recorded Seismograms
(Patrick Small of USC and Ricardo Taborda of UM, 2014)

## Slide 10: Algorithms and Hardware Attributes
Massive I/O requirements
Stencil computations
Nearest neighbor comm.
SCEC Apps
Lustre File System
Node Architecture
3-D Torus Interconnect
HW Systems
Limited
OSTs
Shared
Memories
Machine
Topology
Vector
Capable
Memory
intensive
Comm.
latency
I/O
Throughput
Regular
Comp. pattern
Effective
Buffering
ADIOS
Array
Optimization
Memory Reduction
Cache
Utilization
Node
Mapping
Latency
hiding
Contiguous
I/O access

## Slide 11: AWP-ODC Communication Approach on Jaguar
(Joint work with DK Panda Team of OSU)
(Potluri, S., et al., ICS’10)
Rank placement technique
  Node filling with X-Y-Z orders
  Maximizing intra-node and minimizing inter-node communication
Asynchronous communication
  Significantly reduced latency through local communication
  Reduced system buffer requirement through pre-post receives
Computation/communication overlap
  Effectively hide computation times
  Effective when Tcompute_hide>Tcompute_overhead
  One-sided Communications (on Ranger)

## Slide 12: AWP-ODC Communication Approach on Titan
(Cui et al., SC’13)

## Slide 13: Topology Tuning on XE6/XK7
Matching the virtual 3D Cartesian to an elongated physical subnet prism shape
Maximizing faster connected BW XZ plane allocation
Obtaining a tighter, more compact and cuboidal shaped BW subnet allocation
Reducing inter-node hops along the slowest BW torus Y direction
Joint work with G. Bauer, O. Padron (NCSA), R. Fiedler (Cray) and L. Shih (UH)

## Slide 14: Topology Tuning on Blue Waters
Topology Tuning on XE6/XK7
Matching the virtual 3D Cartesian to an elongated physical subnet prism shape
Maximizing faster connected BW XZ plane allocation
Obtaining a tighter, more compact and cuboidal shaped BW subnet allocation
Reducing inter-node hops along the slowest BW torus Y direction
Joint work with G. Bauer, O. Padron (NCSA), R. Fiedler (Cray) and L. Shih (UH)

## Slide 15: Topology Tuning on Blue Waters
Topology Tuning on XE6/XK7
# nodes | Default | Topaware | Speedup | Efficiency
64 | 4.006 | 3.991 | 0.37% | 100%
512 | 0.572 | 0.554 | 3.15% | 87.5%->90%
4096 | 0.119 | 0.077 | 35.29% | 52.6%->81%
Matching the virtual 3D Cartesian to an elongated physical subnet prism shape
Maximizing faster connected BW XZ plane allocation
Obtaining a tighter, more compact and cuboidal shaped BW subnet allocation
Reducing inter-node hops along the slowest BW torus Y direction

## Slide 16: Two-layer I/O Model
Parallel I/O
  Read and redistribute multiple terabytes inputs (19 GB/s)
    Contiguous block read by reduced number of readers
    High bandwidth asynchronous point-to-point communication redistribution
cores
Shared file

## Slide 17: Two-layer I/O Model
Parallel I/O
  Read and redistribute multiple terabytes inputs (19 GB/s)
    Contiguous block read by reduced number of readers
    High bandwidth asynchronous point-to-point communication redistribution
OSTs
  Aggregate and write

## Slide 18: Two-layer I/O Model
OSTs
Stripe
size
Stripe
size
Stripe
size
…
Temporal aggregator
time step 1
time step 2
… …
time step N
MPI-IO
Parallel I/O
  Read and redistribute multiple terabytes inputs (19 GB/s)
    Contiguous block read by reduced number of readers
    High bandwidth asynchronous point-to-point communication redistribution
  Aggregate and write (10GB/s)
    Temporal aggregation buffers
    Contiguous writes
    Throughput

## Slide 19: Fast X or Fast T
(Poyraz et al., ICCS’’14)

## Slide 20
ADIOS Checkpointing
Problems at M8: system instabilities, 50 TB simulation data
Chino Hills 5Hz simulation is used to validate:
Mesh size: 7000x5000x2500
#cores: 87,500 on Jaguar
WCT: 3 hr
Total timesteps: 40K
3.3 TB simulation data
ADIOS saved checkpoints at 20Kth timestep and validated the outputs at 40Kth timestep
Avg. I/O performance: 22.5 GB/s (compared to 20 GB/s with MPI-IO)
AWP-ODC
ADIOS
Lustre
(Supported by Norbert Podhorszki, Scott Klasky, Qing Liu, ORNL)

## Slide 21: SEISM-IO: IO Library for Integrated Seismic Modeling

## Slide 22: CPUs/GPUs Co-scheduling
aprun -n 50 <GPU executable> <arguments> &
get the PID of the GPU job
cybershake_coscheduling.py:
build all the cybershake input files
divide up the nodes and work among a customizable number of jobs
for each job:
fork extract_sgt.py cores --> performs pre-processing and launches
"aprun -n <cores per job> -N 15 -r 1 <cpu executable A>&"
get PID of the CPU job
while executable A jobs are running:
check PIDs to see if job has completed
if completed: launch
“aprun -n <cores per job> -N 15 -r 1 <cpu executable B>&”
while executable B jobs are running:
check for completion
check for GPU job completion
  CPUs run reciprocity-based seismogram and intensity computations
  Run multiple MPI jobs on compute nodes using Node Managers (MOM)

## Slide 23: Post-processing on CPUs: API for Pthreads
AWP-API lets individual pthreads make use of CPUs: post-processing
  Vmag, SGT, seismograms
  Statistics (real-time performance measuring)
  Adaptive/interactive control tools
  In-situ visualization
  Output writing is introduced as a pthread that uses the API

## Slide 24
Initialize
Calculate SGT
Is the signal received?
Write out - MPI-IO
Is it time to write out?
Initialize simulation
Initialize modules
Start computation on GPU
Specified time step?
Copy velocity data and signal modules
Finalize
More time steps?
Main thread
GPU
Modules on other CPUs on XK7
yes
no
yes
yes
yes
no
no
Initialize

## Slide 25: Probabilistic Seismic Hazard Model
Receiver
Source 1
Source 3
Source 2
M sources to N receivers requires M simulations
Physics-based seismic hazard model requires more than a few earthquake simulations
  Standard “forward” simulation computing 3-component seismograms from M sources at N sites requires M simulations (M > 105, N ~ 103)
  Strain Green tensor based “reciprocal” simulation computing 3-component seismograms for M sources at N sites requires only 3N simulations
  Use of reciprocity reduces CPU time by a factor of ~2,000
Un(r,rs)=Gnj,i(r,rs)Mji
Un(r,rs)=H(rs,r)Mji
H(rs,r)=[Gjn,i(rs,r) + Gin,j(rs ,r)]/2
P(IMk)
P(IMk | Sn)
P(Sn)
Intensity
Measures
Attenuation
Relationship
Earthquake Rupture
Forecast
Probabilistic Seismic Hazard Analysis
M sources to N receivers requires 3N simulations

## Slide 26: CyberShake Calculations
CyberShake contains two phases
Strain Green Tensor (SGT) calculation
  Large MPI jobs
  AWP-ODC-SGT GPU
  85% of CyberShake compute time
Post-processing (reciprocal calculation)
  Many (~400k) serial, high throughput, loosely coupled jobs
  Workflow tools used to manage jobs
Both phases are required to determine seismic hazard at one site
For a hazard map, must calculate ~200 sites

## Slide 27: CyberShake workflows
6 jobs
Mesh generation
Tensor Workflow
1 job
2 jobs
Post-Processing Workflow
.
.
.
DB Insert
Tensor simulation
Tensor extraction
Tensor extraction
Data Products Workflow
Hazard Curve
PMC
SeisPSA
.
.
.
6 PMC jobs
85,000 jobs
SeisPSA
PMC
SeisPSA
SeisPSA
.
.
.
Notes: Green are MPI jobs
Yellow are serial jobs
Tensor workflow runs on Titan, post-processing on Blue Waters or Stampede, data products on SCEC servers

## Slide 28: CyberShake Workflows mapped to Pegasus-MPI-Cluster Jobs
High throughput jobs wrapped in MPI master-worker job

## Slide 29: CyberShake Study 14.2 Metrics
1,144 hazard curves (4 maps) on NCSA Blue Waters
342 hours wallclock time (14.25 days)
46,720 CPUs + 225 GPUs used on average
  Peak of 295,040 CPUs, 1100 GPUs
GPU SGT code 6.5x more efficient than CPU
99.8 million jobs executed (81 jobs/second)
  31,463 jobs automatically run in the Blue Waters queue
On average, 26.2 workflows (curves) concurrently
Notes: Job failure rate: 1.3%

## Slide 30: 1-Hz CyberShake Hazard Curve on Titan
Software: AWP-ODC-GPU
Number of Nodes: 800 XK7 nodes for SGTs, 40 XK7 nodes for velocity mesh
Input data description: 128 GB velocity mesh per site
Simulation wallclock time: 50 minutes for each component
Output data description: 440 GB x 2 components = 880 GB per site
Production setting tested for USC, PAS, SB and WNGC sites
Notes: Job failure rate: 1.3%

## Slide 31
CyberShake 1.0 Hz | XE6 | XK7 | XK7 (CPU-GPU co-scheduling)
Nodes | 400 | 400 | 400
SGT hrs per site | 10.36 | 2.80 | 2.80
Post-processing hours per site** | 0.94 | 1.88 | 2.00
Total Hrs per site | 11.30 | 4.68 | 2.80
Total SUs(Millions)* | 723 M | 299 M | 179 M
SUs saving (Millions) |  | 424 M | 543 M
* Scale to 5000 sites based on two strain Green tensor runs per site ** based on CyberShake 13.4 map
3.7x
speedup
CyberShake SGT Simulations on XK7 vs XE6

## Slide 32: CyberShake SGT Simulations on XK7 vs XE6
CyberShake 1.0 Hz | XE6 | XK7 | XK7 (CPU-GPU co-scheduling)
Nodes | 400 | 400 | 400
SGT hrs per site | 10.36 | 2.80 | 2.80
Post-processing hours per site** | 0.94 | 1.88 | 2.00
Total Hrs per site | 11.30 | 4.68 | 2.80
Total SUs(Millions)* | 723 M | 299 M | 179 M
SUs saving (Millions) |  | 424 M | 543 M
* Scale to 5000 sites based on two strain Green tensor runs per site ** based on CyberShake 13.4 map
3.7x
speedup

## Slide 33
Seismicity-weighted CyberShake grid
Create a broadband CyberShake hazard model for all of California
The statewide CyberShake hazard model will comprise 1.8 billion seismograms
Computational requirements for 1400 sites across California
SCEC CS14.2 study launched on Blue Waters on 18 Feb 2014, 0.5 Hz deterministic, 2 components
  Turnaround: 342 hours
  XE6/XK7 nodes used: 1620, or 49,280 cores
  Jobs submitted: 31,463
  Number of tasks: 470 million
  Storage used: 57 TB
  Allocation hours: 16 M (CPUs + GPUs)
The CS study proposed on Titan for 2014-2015, 1.0 Hz deterministic, 3 components
  Turnaround: 2 days
  XK7 nodes to use: 13,500
  Sustained PFLOP/s: 2.07
  Jobs to submit: 34,263
  Number of tasks: 575 M
  Storage used: 2 PB
  Allocation hours: 20 M (GPUs) + 220 M (CPUs)
The CS study proposed for 2015, 1.5 Hz deterministic + stochastic, 3 components
  Turnaround: 16 days
  XK7 nodes used: 17,400
  Sustained PFLOP: 2.67
  Jobs to submit: 51,000
  Number of tasks: 1.73 billion
  Storage used: 8 PB
  Allocation hours: 160 million (GPUs) + free CPUs
Go Green

## Slide 34
Science Objective:
Creation of 1D mesh BBP etree and mesh on Titan using UCVM.
Computational Information:
(1) Systems Used: Titan
(2) Software Used: UCVM
(3) Number of Nodes/GPU/Cores: 512 cores on 32 nodes (16 cores/node)
(4) Input Data Description: 1M Configuration, 1G
(5) Simulation Runtime: 40 minutes
(6) Output Data Description: etree containing 180km x 110km x 50 km (110GB file)
UCVM Code development bbp 1D mesh

## Slide 35
Science Objective:
Compare impact of 1D ground motion simulations to 3D ground motion simulations when used in Broadband validation tests.
Computational Information
Systems Used: Titan
Software Used: Hercules GPU
(3) Number of Nodes/GPU/Cores: 800 GPUs (SGTs), 640 CPUs (velocity mesh)
(4) Input Data Description: 120 GB velocity mesh per Site
(5) Simulation Runtime: 50 minutes for each component
(6) Output Data Description: 440 GB x 2 components = 880 GB per Site
Chino Hills 1Hz (Hercules) BBP with Extended Sources

## Slide 36: Broadband Platform Overview
Broadband Platform Software Distributions:
  Source Codes and Input Config Files : 2G (increases as platform runs)
  Data Files (Greens Functions) : 11G (static input files)

## Slide 37
GP RupGen
GP LowFreq
GP HiFreq
GP GOF
RotD50
RotD50
LOMAP.src
LOMAP.srf
SynthLoFreq.bbp
SynthHiFreq.acc.bbp
Synth.rd50
BiasPlot
ObsFormat.acc
Obs.rd50
Observed Data Processing
Simulation Data Processing
Obs_corrected.rd50
SiteCorrect
AriasDur
Common
Post-Processing
Utilities

## Slide 38
GP RupGen
Hercules 3D
GP HiFreq
GP GOF
RotD50
RotD50
LOMAP.src
LOMAP.srf
SynthLoFreq.bbp
SynthHiFreq.acc.bbp
Synth.rd50
BiasPlot
ObsFormat.acc
Obs.rd50
Observed Data Processing
Simulation Data Processing
Obs_corrected.rd50
SiteCorrect
AriasDur
Common
Post-Processing
Utilities

## Slide 39: Looking ahead: Extreme Scale Earthquake Problems
Dynamic rupture simulations
  Current 1D outer/inner scale: 6x105
  Target: 1D 600000m/0.001m (6x108)
Wave propagation simulations
  Current 4D scale ratio: 1x1017
  Target 4D scale ratio: 3x1023
Data-intensive simulations
  Current tomography simulations: ~ 0.5 PB
    SCEC 2015-2016 INCITE plan to carry out 5 iterations, 1.9 TB for each seismic source, total 441 TB for the duration of the inversion alone
  Target tomography simulations:~ 32 XBs

## Slide 40: Outer/inner Scale Ratio of SCEC Computational Requirements

## Slide 41: SCEC Computational Plan 2015-2016

## Slide 42: SCEC Software Development
Advanced algorithms
  Development of Discontinuous Mesh AWP
  Fractal distribution and strike-slip acceleration
  Small-sale heterogeneities
  Frequency-dependent attenuation
  Include near-surface low-velocity material up to higher frequencies than previously possible
  High-F simulation of ShakeOut scenario 0-4Hz
Prepare SCEC HPC codes for next-generation systems
  Programming model
    Three levels of parallelism to address accelerating technology
    Portability
    Avoid communication and power dominating design
    Data locality
  Automation: Enable workflows on advanced systems
  I/O and fault tolerance
    Data scaling to perform more work per unit data movement
    Deal with heterogeneous architectures and tiered storage
    Data reduction methods and caching algorithms to move in/out data from dynamic storage
    Fault tolerance
  Performance: topology mapping on Titan, parallel threads implementation, and load balancing
  Scaling: dealing with million-way concurrency, strong + weak scaling
  New architectures: prepare mini-application to support new processors and interconnects

## Slide 43: Computing at Extreme Scale
Top 500 No. 1 Peak Capability
Peak DOE Capability
Sustained NSF
Peak NSF
Sustained DOE
Year
Chart: 
| 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 |  | 2011 | 2012 |  | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
 | 36 | 91.8 | 183 | 367 | 367 | 367 | 367 | 596 | 1375 | 1456 | 1456 | 2331 | 2331 | 4701 | 8773 | 11280 | 20132 | 27112 | 54902 | 54902 | 0
 | 41 | 70.8 | 136 | 280 | 280 | 280 | 280 | 478 | 1026 | 1105 | 1105 | 1759 | 1759 | 2566 | 8162 | 10511 | 16324 | 17590 | 33862 | 33862 | 0
 | 15.3 | 15.3 | 15.3 | 15.3 | 15.3 | 55.5 | 90 | 90 | 607 | 607 | 607 | 1028 | 1028 | 1028 | 1173 | 1173 | 1173 | 3959 | 8520 | 8520
 | 9.8 | 9.8 | 9.8 | 9.8 | 9.8 | 41.5 | 63 | 63 | 463 | 463 | 463 | 831 | 831 | 831 | 919 | 919 | 919 | 2660 | 5168 | 5168
 | 22.94 | 91.8 | 183 | 367 | 367 | 367 | 367 | 596 | 1375 | 1456 | 1456 | 2331 | 2331 | 2331 | 2331 | 2331 | 20132 | 27112 | 27112 | 27112
 | 19.94 | 70.8 | 136 | 280 | 280 | 280 | 280 | 478 | 1026 | 1105 | 1105 | 1759 | 1759 | 1759 | 1759 | 1759 | 16324 | 17590 | 17590 | 17590
 | 0.04 | 0.68 | 7.3 | 27 | 223 | 0 | 2230 | 2760 | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 23595 | 0 | 118478 | 0 | 758263 | 0

## Slide 44: Computing at Extreme Scale
Chart: 
| 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 |  | 2011 | 2012 |  | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
 | 36 | 91.8 | 183 | 367 | 367 | 367 | 367 | 596 | 1375 | 1456 | 1456 | 2331 | 2331 | 4701 | 8773 | 11280 | 20132 | 27112 | 54902 | 54902 | 0
 | 41 | 70.8 | 136 | 280 | 280 | 280 | 280 | 478 | 1026 | 1105 | 1105 | 1759 | 1759 | 2566 | 8162 | 10511 | 16324 | 17590 | 33862 | 33862 | 0
 | 15.3 | 15.3 | 15.3 | 15.3 | 15.3 | 55.5 | 90 | 90 | 607 | 607 | 607 | 1028 | 1028 | 1028 | 1173 | 1173 | 1173 | 3959 | 8520 | 8520
 | 9.8 | 9.8 | 9.8 | 9.8 | 9.8 | 41.5 | 63 | 63 | 463 | 463 | 463 | 831 | 831 | 831 | 919 | 919 | 919 | 2660 | 5168 | 5168
 | 22.94 | 91.8 | 183 | 367 | 367 | 367 | 367 | 596 | 1375 | 1456 | 1456 | 2331 | 2331 | 2331 | 2331 | 2331 | 20132 | 27112 | 27112 | 27112
 | 19.94 | 70.8 | 136 | 280 | 280 | 280 | 280 | 478 | 1026 | 1105 | 1105 | 1759 | 1759 | 1759 | 1759 | 1759 | 16324 | 17590 | 17590 | 17590
 | 0.04 | 0.68 | 7.3 | 27 | 223 | 0 | 2230 | 2760 | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 23595 | 0 | 118478 | 0 | 758263 | 0
Top 500 No. 1 Peak Capability
Peak DOE Capability
Sustained NSF
Peak NSF
Sustained DOE
Year
Sustained SCEC measured performance for a single milestone capability simulation

## Slide 45
Chart: 
| 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 |  | 2011 | 2012 |  | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
 | 36 | 91.8 | 183 | 367 | 367 | 367 | 367 | 596 | 1375 | 1456 | 1456 | 2331 | 2331 | 4701 | 8773 | 11280 | 20132 | 27112 | 54902 | 54902 | 0
 | 41 | 70.8 | 136 | 280 | 280 | 280 | 280 | 478 | 1026 | 1105 | 1105 | 1759 | 1759 | 2566 | 8162 | 10511 | 16324 | 17590 | 33862 | 33862 | 0
 | 15.3 | 15.3 | 15.3 | 15.3 | 15.3 | 55.5 | 90 | 90 | 607 | 607 | 607 | 1028 | 1028 | 1028 | 1173 | 1173 | 1173 | 3959 | 8520 | 8520
 | 9.8 | 9.8 | 9.8 | 9.8 | 9.8 | 41.5 | 63 | 63 | 463 | 463 | 463 | 831 | 831 | 831 | 919 | 919 | 919 | 2660 | 5168 | 5168
 | 22.94 | 91.8 | 183 | 367 | 367 | 367 | 367 | 596 | 1375 | 1456 | 1456 | 2331 | 2331 | 2331 | 2331 | 2331 | 20132 | 27112 | 27112 | 27112
 | 19.94 | 70.8 | 136 | 280 | 280 | 280 | 280 | 478 | 1026 | 1105 | 1105 | 1759 | 1759 | 1759 | 1759 | 1759 | 16324 | 17590 | 17590 | 17590
 | 0.04 | 0.68 | 7.3 | 27 | 223 | 0 | 2230 | 2760 | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 23595 | 0 | 118478 | 0 | 758263 | 0
Top 500 No. 1 Peak Capability
Peak DOE Capability
Sustained NSF
Peak NSF
Sustained DOE
Sustained SCEC High-F
Year
High-F + small-scale heterogeneities
High-F + plasticity
High-F + topo
High-F + lower Vsmin
High-F + Q (f)
Sustained SCEC measured performance for a single milestone capability simulation
Computing at Extreme Scale

## Slide 46: Computing at Extreme Scale
Chart: 
| 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 |  | 2011 | 2012 |  | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
 | 36 | 91.8 | 183 | 367 | 367 | 367 | 367 | 596 | 1375 | 1456 | 1456 | 2331 | 2331 | 4701 | 8773 | 11280 | 20132 | 27112 | 54902 | 54902 | 0
 | 41 | 70.8 | 136 | 280 | 280 | 280 | 280 | 478 | 1026 | 1105 | 1105 | 1759 | 1759 | 2566 | 8162 | 10511 | 16324 | 17590 | 33862 | 33862 | 0
 | 15.3 | 15.3 | 15.3 | 15.3 | 15.3 | 55.5 | 90 | 90 | 607 | 607 | 607 | 1028 | 1028 | 1028 | 1173 | 1173 | 1173 | 3959 | 8520 | 8520
 | 9.8 | 9.8 | 9.8 | 9.8 | 9.8 | 41.5 | 63 | 63 | 463 | 463 | 463 | 831 | 831 | 831 | 919 | 919 | 919 | 2660 | 5168 | 5168
 | 22.94 | 91.8 | 183 | 367 | 367 | 367 | 367 | 596 | 1375 | 1456 | 1456 | 2331 | 2331 | 2331 | 2331 | 2331 | 20132 | 27112 | 27112 | 27112
 | 19.94 | 70.8 | 136 | 280 | 280 | 280 | 280 | 478 | 1026 | 1105 | 1105 | 1759 | 1759 | 1759 | 1759 | 1759 | 16324 | 17590 | 17590 | 17590
 | 0.04 | 0.68 | 7.3 | 27 | 223 | 0 | 2230 | 2760 | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 23595 | 0 | 118478 | 0 | 758263 | 0
Top 500 No. 1 Peak Capability
Peak DOE Capability
Sustained NSF
Peak NSF
Sustained DOE
Year
High-F + small-scale heterogeneities
High-F + plasticity
High-F + topo
High-F + lower Vsmin
High-F + Q (f)
Sustained SCEC High-F
CyberShake (CS) Disiderata predicted sustained performance for 4,000 sites required to generate 1.0-Hz, 1.5-Hz and 2.0-Hz state-wide seismic hazard map normalized to 24-hr completion
Sustained SCEC measured performance for a single milestone capability simulation
Notes: Timeline of the SCEC milestone runs, comparing performance requirements with DOE INCITE and NSF XSEDE/TeraGrid top high-end system. Previous TeraShake (TS1, TS2), ShakeOut (SO-K, SD-D), M8, Chino Hills 5-Hz (CH-5Hz), Rough Fault 10-Hz (RH-10Hz), and single CyberShake SGT CS-0.5Hz, future CS-1.0Hz, CS-1.5Hz, CS-2.0Hz runs are shown for comparison. Yellow circles are required sustained performance to enable completion of 4,000 sites simulations normalized to 24-hr run

## Slide 47: Computing at Extreme Scale
Chart: 
| 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 |  | 2011 | 2012 |  | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
 | 36 | 91.8 | 183 | 367 | 367 | 367 | 367 | 596 | 1375 | 1456 | 1456 | 2331 | 2331 | 4701 | 8773 | 11280 | 20132 | 27112 | 54902 | 54902 | 0
 | 41 | 70.8 | 136 | 280 | 280 | 280 | 280 | 478 | 1026 | 1105 | 1105 | 1759 | 1759 | 2566 | 8162 | 10511 | 16324 | 17590 | 33862 | 33862 | 0
 | 15.3 | 15.3 | 15.3 | 15.3 | 15.3 | 55.5 | 90 | 90 | 607 | 607 | 607 | 1028 | 1028 | 1028 | 1173 | 1173 | 1173 | 3959 | 8520 | 8520
 | 9.8 | 9.8 | 9.8 | 9.8 | 9.8 | 41.5 | 63 | 63 | 463 | 463 | 463 | 831 | 831 | 831 | 919 | 919 | 919 | 2660 | 5168 | 5168
 | 22.94 | 91.8 | 183 | 367 | 367 | 367 | 367 | 596 | 1375 | 1456 | 1456 | 2331 | 2331 | 2331 | 2331 | 2331 | 20132 | 27112 | 27112 | 27112
 | 19.94 | 70.8 | 136 | 280 | 280 | 280 | 280 | 478 | 1026 | 1105 | 1105 | 1759 | 1759 | 1759 | 1759 | 1759 | 16324 | 17590 | 17590 | 17590
 | 0.04 | 0.68 | 7.3 | 27 | 223 | 0 | 2230 | 2760 | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 23595 | 0 | 118478 | 0 | 758263 | 0
Top 500 No. 1 Peak Capability
Peak DOE Capability
Sustained NSF
Peak NSF
Sustained DOE
CyberShake Disiderata
Year
High-F + small-scale heterogeneities
High-F + plasticity
High-F + topo
High-F + lower Vsmin
High-F + Q (f)
Sustained SCEC High-F
CyberShake (CS) Disiderata predicted sustained performance for 4,000 sites required to generate 1.0-Hz, 1.5-Hz and 2.0-Hz state-wide seismic hazard map normalized to 24-hr completion
Sustained SCEC measured performance for a single milestone capability simulation

## Slide 48: Acknowledgements
Collaborators
Matthew Norman, Jack Wells, Judith Hill (ORNL), Carl Ponder, Cyril Zeller, Stanley Posey and Roy Kim (NVIDIA), Jeffrey Vetter, Mitch Horton, Graham Lopez, Richard Glassbrook (NICS), DK. Panda and Sreeram Potluri (OSU), Gregory Bauer, Jay Alameda, Omar Padron (NCSA); Robert Fiedler (Cray), Liwen Shih (UH)
Computing Resources
NCSA Blue Waters, OLCF Titan, XSEDE Keeneland, NVIDIA GPUs donation to HPGeoC/SDSC
NSF Grants
NCSA NEIS-P2/PRAC OCI-0832698, XSEDE ECCS, PRAC, SI2-SSI (OCI-1148493 ), Geoinformatics (EAR-1226343), NSF/USGS SCEC4 Core (EAR-0529922 and 07HQAG0008)

## Slide 49: End