## Slide 1: Updates on CyberShake Ground Motion Simulations for Southern California
Scott Callaghan, Philip J. Maechling, Fabio Silva, Kevin R. Milner, Mei-Hui Su, Christine A. Goulet, Kim B. Olsen, Te-Yang Yeh, Robert W. Graves, Karan Vahi, Ewa Deelman, Albert Kottke, Thomas H. Jordan, and Yehuda Ben-Zion
NGA-W3 meeting
Thursday, November 9, 2023

## Slide 2: CyberShake Overview
SCEC’s 3D physics-based probabilistic seismic hazard analysis (PSHA) platform
Earthquake Rupture Forecast (ERF) provides list of relevant events with probabilities
  625,000 events per site
Reciprocity-based approach to simulate low-frequency seismograms
Intensity measures derived from seismograms
Hazard results from individual sites interpolated with GMM basemap

## Slide 3
Uniform California Earthquake Rupture Forecast
UCVM
AWP-ODC-SGT wave propagation
Low-frequency seismogram synthesis
High-frequency seismogram synthesis (BBP)
Merge and combine
Aggregate data products
Velocity Mesh
600,000+ events
Graves & Pitarka kinematic rupture generator
Intensity measures
0-1 Hz low-frequency seismograms
RotD50, PGA, PGV
Low-frequency CyberShake workflow
Broadband CyberShake workflow
Hazard Map
1-50 Hz seismograms
0-50 Hz broadband data products
RotD50, PGA, PGV
Hazard Curve

## Slide 4: New Features in CyberShake Study 22.12
Update to Study 15.4 and 15.12
Broadband simulations
  Validated against historic events
Modifications to 3D velocity model
  Goal is to resolve issues with high velocities at the surface
Updates to rupture generation for individual events
  Migration to more recent kinematic rupture code
  Sampling of additional variability

## Slide 5: Broadband Validation
Selected validation events from the SCEC Broadband Platform
  Northridge, Whittier, Chino Hills, Landers
64 realizations created for each event
  Hypocenter and magnitude preserved
  Different slip realizations
  GP rupture generator used
CyberShake pipeline run for sites with recordings in BBP
  Usually ~40 stations per event
Calculate metrics
3 slip realizations for 1994 Northridge

## Slide 6: Validation Metrics
Looking at BBP goodness-of-fit metric
  Both overall GoF (all sites, all realizations) and best realization
  Compare 3D CyberShake, 1D BBP, and GMMs to observations
Show that CyberShake works
  Reasonable ground motions for both historic and hypothetical events
Wiggle-to-wiggle agreement not the goal
  Can get very good low-frequency agreement with tuning
  Here, want to validate entire method on known and unknown events
  Goal is to get reasonable results on realization sweeps

## Slide 7: Northridge
3D CyberShake
1D BBP
GMMs
Overall GoF
Best Realization

## Slide 8: Landers (multi-segment)
3D CyberShake
1D BBP
GMMs
Overall GoF
Best Realization

## Slide 9: Velocity Model Merged Taper
500
1000
2500
Previous studies used CVM-S4.26.M01
  Tomography model + near-surface layer
  High Vs values outside of basins
Used Ely-Jordan approach to apply Vs30- based taper down to 700m (Hu et al. 2022)
  Using taper, determine Vp, Vs, rho values at each grid point in the mesh
  Compare taper and non-taper Vs value
  Select smaller Vs value (and corresponding Vp and rho) to preserve basins
CVM-S4.26.M01, surface Vs
USC
LAPD

## Slide 10: Site Velocity Profiles
USC (in basin)
CVM-S4.26.M01
700m taper
Merged taper
LAPD (outside basin)
Taper is selected at all depths to 700m
Vs30: 2573 m/s -> 400 m/s
Z1.0: 0m -> 110m
Taper is only selected at surface point
Vs30: 500 m/s -> 500 m/s
Z1.0: 580m -> 580m
~2500 m/s
~400 m/s
500 m/s
<500 m/s

## Slide 11: Merged Taper Cross-sections
Surface
300m depth
CVM-S4.26.M01
Merged Taper
% difference
500
1000
2500
500
1000
2500
-100%
0%
100%
500
1000
2500
500
1000
2500
-100%
0%
100%

## Slide 12: Updates to Rupture Generation
New version of GP generator (v5.5.2, same as in latest BBP release)
  Reduced correlation between slip and risetime
  Reduced shallow fault rupture speed
  Slightly weaker directivity
  Variable strike & dip
  Increased energy at 2-3 sec
Rupture velocity is no longer fixed
  67.5%-87.5% of shear wave velocity
Denser hypocentral spacing
  4.5 km -> 4 km
  ~31% increase in rupture variations
Slip plot, v3.3.1 from Study 15.4 (top); v5.5.2 from Study 22.12 (bottom)

## Slide 13: Rupture Generator Impact on Ground Motions
WNGC
PAS
10 sec
5 sec
3 sec
2 sec

## Slide 14: Rupture Generator Impact on Hazard
WNGC
PAS
10 sec
5 sec
3 sec
2 sec
Study 15.4 rupture generator (v3.3.1)
Study 22.12 rupture generator (v5.5.2)

## Slide 15: Study 22.12 Statistics
335 sites around SoCal
Study performed over 76 days
772,000 node-hrs on OLCF Summit
  Averaged 422 nodes
  Max of 3382 (73% of Summit)
Managed ~2.5 PB of data
74 TB of data staged back to archival storage
  420 million two-component low-frequency and broadband seismograms
  83 billion intensity measures and durations
Study 22.12 site map

## Slide 16: Change in Hazard, non-basin sites
LAPD
s035
s764
s211
3 sec curves
Study 15.4
Study 22.12

## Slide 17: Change in Hazard, basin sites
3 sec curves
Study 15.4
Study 22.12
s117
WNGC
USC
SBSM

## Slide 18: Study 22.12: Low-Frequency Curves
USC (inside basin)
LBUT (outside basin)
5 sec RotD50
3 sec RotD50
2 sec RotD50
10 sec RotD50
Red: Study 15.4
Black: Study 22.12

## Slide 19: Low-Frequency Results
2 sec, RotD50
10 sec, RotD50
Study 22.12
Ratio, 22.12/15.4
Ratio, 22.12/GMMs

## Slide 20: Study 22.12: Broadband Results
0.1 sec, RotD50
0.5 sec, RotD50
Study 22.12
Ratio, 22.12/15.12
Distribution of z-scores between 22.12 BB and ASK2014

## Slide 21: Study 22.12: Data Access
Developed CyberShake data access tool
  Python-based
  Asks user series of questions
  Applies filters to select subset
Simplifies access to variety of CyberShake data products
  Site metadata
  Event metadata
  Intensity measures
  Seismograms
Available on github: https://github.com/SCECcode/cs-data-tools/

## Slide 22: Next Study
Preparing for Study 24.1
  Greater Bay Area
  Similar to Study 22.12
  Just got the compute time this week!
Currently evaluating 3D velocity models
Will validate with Central and Northern CA BBP validation events
Study 24.1 site map

## Slide 23: Future Plans
Increase deterministic frequency to 2 Hz
  Frequency-dependent attenuation
  Small-scale velocity heterogeneities
Include nonlinear simulations
  Reciprocity is by definition linear
  Identify subset of events for full nonlinear simulations
  Apply pseudo-nonlinearity to reciprocity results
Streamline process of integrating new codes and models
  Goal is to support multiple codes for each stage
  Supports improved quantification of uncertainty

## Slide 24: Thanks!