CyberShake UCERF3:
Downsampling Tests
Scott Callaghan
CyberShake/High-F Workshop
June 8, 2016

---
Downsampling Test Steps
1. Simulate SGTs on statewide volume, for Southern California site (USC)
2. Perform reciprocity on events which span creeping section
3. Perform reciprocity events only south of Parkfield
4. For Southern California locations, do south-of-Parkfield events look (approximately) the same as north-of-Parkfield events which extend southward?

---
SGT Status
Simulate SGTs on statewide volume, for Southern California site (USC)
    - This proved more difficult than anticipated
    - Stitched together
      - CVM-S5
      - USGS Bay Area
      - 1D background
    - Ran forward sim across interface to check for reflections

---
UCERF 3 SAF rupture (0.25 Hz)

---
Reciprocity status
1. Perform reciprocity on events which span Parkfield
2. Perform reciprocity events only south of Parkfield
- Currently running on Blue Waters; some technical challenges due to larger (3x points) faults
- When complete, will compare outputs
  - Seismograms
  - PSA: Geometric mean and RotD100
- Will calculate hazard curves with and without downsampling