CyberShake Study 22.12
Science Readiness Review
Scott Callaghan
Southern California Earthquake Center

---
Study 22.12 Scientific Goals
Perform an updated Broadband CyberShake calculation in Southern California.
First since Study 15.12
BBP v22.4 codes used for high-frequency calculation
Calculate CyberShake results with a modified velocity model.
Merged taper model, using CVM-S4.26.M01 with the Ely-Jordan taper to 700m
Use an updated version of the Graves & Pitarka rupture generator
V5.5.2, same as is used in the BBP v22.4
Includes sampling of variability in rupture velocity
Denser hypocentral spacing (4.5 km to 4 km) → 31% more variations/site
04/11/2023

---
Proposed Study sites
Same 335 sites as were used in Study 21.12
Site calculation order:
Standard 10 (USC, PAS, LADT, LBP, WNGC, SABD, SBSM, FFI, CCP, SMCA)
20 km grid
10 km grid
Additional POIs, PBRs,
broadband stations
5 km grid sites

---
Study 22.12 Data Products
Two-component seismograms (626k/site x 335 sites x 2 = 420 million)
Intensity measures
Deterministic
RotD50 and 100 at 25 periods (1-20 sec) + PGV
(https://strike.scec.org/scecpedia/CyberShake_Study_22.12#Deterministic)
2, 3, 4, 5, 7.5, and 10 sec for RotD50 and RotD100 stored in DB
Broadband
RotD50 and 100 at 66 periods (0.01-20 sec) + PGA, PGV
(https://strike.scec.org/scecpedia/CyberShake_Study_22.12#Broadband)
19 periods, PGA, PGV stored in DB
Duration metrics (same for both deterministic and broadband)
Energy integral, Arias intensity, cumulative absolute velocity, significant durations (5-75%, 5-95%, 20-80%) for velocity and acceleration and X and Y
Acceleration 5-75% and 5-95% for X and Y stored in DB
Hazard curves for 335 sites (0.1, 0.2, 0.5, 1, 2, 3, 4, 5, 7.5, 10 sec)
RotD50 hazard maps at 0.1, 0.2, 0.5, 1, 2, 3, 5, and 10 sec

---
Velocity Model
Modification to velocity model generation to reduce high near-surface values outside of basins
For mesh points in the top 700m:
Query CVM-S4.26.M01 model
Calculate the velocity values using the Ely-Jordan taper, with a depth of 700m
Select the approach which produces the smaller Vs value
For deeper points, just use CVM-S4.26.M01
Vp/Vs ratio is now preserved
If Vs floor (500 m/s) is applied, Vp is scaled to preserve ratio
Surface point is populated by querying at depth 25m

---
CVM-S4.26.M01
Merged taper
Percent difference
Surface (25m)
100m
Additional cross-sections available at https://strike.scec.org/scecpedia/CyberShake_Study_22.12#Cross-sections

---
Taper
Merged Taper
CVM-S4.26.M01
Taper
Merged Taper
CVM-S4.26.M01
USC
(in basin)
SBSM
(in basin)
PERR (out of basin)
LAPD (out of basin)
s035 (out of basin)
MRVY (out of basin)

---
Impact on Hazard

---
Rupture Generator
Originally looked at GP v5.4.2
Produced larger-than-expected ground motions at 2-3 sec for M8+ sSAF events
WNGC, 3 sec, v3.3.1 vs v5.4.2
WNGC, 3 sec, v3.3.1(blue) vs v5.4.2 (red)

---
Rupture Generator
Updated to GP v5.5.2
Correlates risetime and slip more strongly
Modified risetime value of 2.3 (slower risetimes)
Produced reduced ground motions in keeping with expectations
PAS, v3.3.1 (blue), v5.4.2 (red), v5.5.2 (yellow)
WNGC, v3.3.1 (blue), v5.4.2 (red), v5.5.2 (yellow)
WNGC, 3 sec, v3.3.1 vs v5.5.2

---
Spectral Discontinuity
Study 15.12 spectral discontinuities around 1 Hz seem resolved
Rupture variations at 3 sec geo mean within 1% of target (dark gray)
All rupture variations (light gray)
Improvements due to combo of rupture generator and HF code
WNGC from Study 15.12
WNGC, Study 22.12 config
USC, Study 22.12 config

---
Rupture Velocity
Previous CyberShake studies used constant rvfrac=0.8
BBP has moved to sampling rvfrac from distribution
Uniformly distributed from [0.675, 0.875]
To ensure reproducibility, we specify rvfrac
Calculate it using BBP codes
Store in database, for each variation
Pass into rupture generator when variations are created
Use similar process for random seed

---
Validation
Extensive validation against BBP and historic events has been performed throughout the study development
Northridge, Chino Hills, Whittier, Landers
Steps in validation documented at https://strike.scec.org/scecpedia/Broadband_CyberShake_Validation
Northridge (previous HF code)
Northridge and Landers (single-segment) rerunning with study config
Best CS realization

---
Study 22.12 Parameters
1.0 Hz deterministic
100 m grid spacing
50 km depth
SGT dt = 0.005 sec, nt = 40000 timesteps (200 sec) for most, 60000 timesteps/300 sec if any hypocenter-site distances are greater than 450 km
Source filtered at 2 Hz
Seismogram dt=0.05, nt = 8000 timesteps (400 sec)
50 Hz stochastic
Seismogram dt=0.01, nt=40000 timesteps (400 sec)
High-frequency code hb_high v6.1.1
Merging performed over range (~0.9-1.1 Hz)
Site adjustments applied based on Vs30
UCERF 2 ERF
Graves and Pitarka (2022) rupture generator

---
Computational Plan
Perform 20-site stress test
Calculate SGTs for remaining 315 sites
Calculate low-frequency post-processing for remaining 315 sites – this will use our remaining Summit allocation
Best to calculate this entirely on Summit, so SGTs don’t have to be transferred.
If we can, run broadband calculations on Summit
If OLCF cuts us off, run broadband calculations on Frontera

---
Storage Requirements
Summit (learned from Study 21.12 that no quotas are enforced on scratch)
507 TB SGTs
553 TB temporary data
73 TB output data
CARC
73 TB output files to project storage
66 TB free; will migrate additional pre-Study 15.4 data to OLCF HPSS
Database on moment.usc.edu
654 GB needed; moment has 379 GB on disk + 846 GB in database free
Shock-carc workflow submission host
737 GB workflow logs (1.5 TB free)

---
Estimated Duration
At Study 21.12 throughput rates:
116 days to use up Summit allocation
252 days to finish study
Anticipate higher throughput on Summit due to job bundling
At Study 21.12 percentage of system usage, 88 days to complete broadband calculations on Frontera
Overall estimated duration of 90 days on Summit + 88 days on Frontera with 30 days overlap = 150 days.

---
Risks
Storage on Summit
~460 TB for SGTs for 315 sites
May need to temporarily store them elsewhere (OLCF HPSS, CARC scratch, TACC Ranch)
Storage on CARC
Plan to migrate more data to OLCF HPSS (can move ~1.5 TB/day)
After study completes, investigate data compression for seismograms
Limited compute time on Summit
Move calculations to Frontera
Additional resources include CARC, Expanse, Perlmutter, Delta
Reduced support during holidays

---
Action Items
Finish and share Northridge and Landers validation results with Study 22.12 configuration